Radio Remote Operation and Installation

OPERATION

Button 1 – Off

Button 2 – Blower On

Button 3 – Blower and Feeder On

To start machine

- Press button 2 then 3.

To turn off feeder only

- Press button 3 again.

To turn off blower and feeder

- Press Button 1.

INSTALLATION – MACHINE WITH EMERGENCY STOP BUTTON

- Remove knockout cover to expose hole in bottom of box and install pigtail cord in hole.

- Attach green wire to ground screw (upper right corner) along with other green wire.

- Install black wire with red wire in the top screw of emergency stop button.

- Screw or bolt remote receiver to a protected area in the truck.

- Plug in two cords.

- You’re ready to go!

INSTALLATION – MACHINE WITHOUT EMERGENTY STOP BUTTON

- Drill 7/8” hole through the bottom of the remote control box.

- Install pigtail cord. Tighten locknut firmly.

- Attach green wire to the ground screw (upper right corner) and splice black wire into white or red wire in box.

- Screw or bolt remote receiver to a protected area in the truck.

- Plug in two cords.

- You’re ready to go!